Verification and Upgrade of NATL’s 50x50m Gridpoints

During the fall of 2012, Amanda Abel and Ethan Carter, helped by Tom Walker, located 83 surveyed gridpoints in NATL-west and 12 surveyed gridpoints in NATL-east.  At each gridpoint they attempted to locate the iron pin that the student surveyors had installed in 1999. At that time the location and identity of each gridpin was made evident by a 40-inch long, 1-inch inside-diameter gridstake with the gridpin within.  When no pin was found within or very near the gridstake, the approximate position of the missing pin was determined by measuring from neighboring gridpins and using lines-of sight along established gridlines.  Digging at the estimated position located all missing gridpins except the one at gridpoint  E3 (Fig. 1).  At E3’s estimated position a 12-inch long, threaded, ½-inch diameter steel rod was driven slightly below the soil surface.  In one instance (Fig. 1), the distance between original gridpins was other than 50m:  G5 and G6 were separated by 50m plus ca. 10cm (4 inches). At every gridpoint a 5-ft long flag holder with a ¾-inch inside diameter was driven into the ground in contact with the north side of the gridstake.  The flag holder and gridstake were strapped together near the top with a stainless steel pipe clamp, taking care to keep the bundle of the two perpendicular to the soil surface.  At grid points where the gridstakes were steel (to prevent damage from controlled burns), electrical metallic tubing [EMT] was used for the flag holders. Elsewhere schedule 40 PVC pipe was used.  The lower end of each flag holder was cut at a 40 degree angles to make it easier to drive into the ground.  A 10-ft piece of ½ inch EMT with fire-orange flagging at top and at 1m below was inserted in each flag holder

Figure 1: Location of the installed proxy gridpin (E3) indicated with red dot.  A distance 
between gridpins of >50m is indicated by a dotted red line between G5 and G6.