NATL-east Walkway Section

16 Oct 2008 plans [with notes as to as-built modifications]

Notes

All wood is pressure treated.

The walkway is 217 feet long and is supported on its east side by 4x4 fence posts at intervals of about 7.5 ft.

Opposite each fence post is a 4x4 piling, sharpened to a 45-degree point that that will be driven with a sledge hammer 3ft into firm substrate or to the point of refusal.  A steel cap will protect the top of the piling during driving.

Two 2x10x32” ledgers will be attached to each pair of 4x4 uprights with four 7”x 3/8”-dia stainless steel bolts (w/ washers).

Where east-west bracing is needed, a 2x4x36” will be attached beneath the ledgers with two 4”x 3/8-dia stainless steel lag bolts (w/ washers). [none was needed]

Stringers are 2”x6” actual and made by gluing together pairs of 15-16ft boards salvaged from corral fencing. [middle stringer was omitted and east stringer was attached to 2x4 blocks attached to fence posts]

Stringers end at ledger-pairs and are staggered.

Stringers are made into three continuous beams by 4.5” lap joints at ends (glued and screwed).

Stringers are attached to ledgers with hurricane anchors secured by galv. nails. [not needed]

Outside stringers are attached to pilings with 3.5” coated screws. [east stringers screwed to blocks]

Boxing is inserted between stringers at each ledger pair and toe-nailed in with galv. nails. [not needed]

Decking is attached to stringers with 2.5” coated screws.

[Transverse decking cut from salvaged lumber was substituted for longitudinal decking.]

Railing is attached to fence posts with 3.5” coated screws.

Where north-south bracing is needed, a diagonal 2x4 brace will be installed from just beneath the railing on one post to just above the decking on an adjacent post [not needed].